SECTION 06 40 00 / 12 36 00

PAPER COMPOSITE COUNTERTOPS

PART 1  GENERAL

1.01	SECTION INCLUDES

A.	Countertops and windowsills for architectural cabinetwork.

B.	Wall-hung counters and vanity tops.

1.02	RELATED REQUIREMENTS

A.	Section 06 40 00 - Architectural Millwork / Section 12 36 00 - Countertops.

B.	Section 22 40 00 - Plumbing Fixtures:  Sinks.

1.03	REFERENCE STANDARDS

A.	ISSFA-2 - Classification and Standards for Solid Surfacing Material; International Solid Surface Fabricators Association; 2001 (2002)

B.	NEMA LD 3 - High-Pressure Decorative Laminates; 2005.

1.04	SUBMITTALS

A.	See Section [__ __ __] - Submittals, for submittal procedures.

B.	Product Data:  Manufacturer's data sheets on each product to be used, including:

1.	Preparation instructions and recommendations.

2.	Storage and handling requirements and recommendations.

3.	Specimen warranty.

C.	Shop Drawings:  Complete details of materials and installation; combine with shop drawings of cabinets and casework specified in other sections.

D.	Verification Samples:  For each finish product specified, minimum size 3 inches (94 mm) square, representing actual product, color, and patterns.

E.	Test Reports:  Chemical resistance testing, showing compliance with specified requirements.

F.	LEED Submittals:

1.	Cost: provide material cost of counters, and engineered wood substrate.

2.	VOCs: submit product name and manufacturer of adhesives and sealants applied on-site and LEED Prohibited Content Form, [__ __ __].

3.	Engineered wood products: submit complete LEED Prohibited Content Form, [__ __ __].

G.	Maintenance Data:  Manufacturer's instructions and recommendations for maintenance and repair of countertop surfaces.

1.05	QUALITY ASSURANCE

A.	Fabricator Qualifications:  North Star Surfaces approved.

B.	Installer Qualifications:  North Star Surface approved.

1.06	DELIVERY, STORAGE, AND HANDLING

A.	Store products in manufacturer's unopened packaging until ready for installation.

B.	Store and dispose of solvent-based materials, and materials used with solvent-based materials, in accordance with requirements of local authorities having jurisdiction.

1.07	FIELD CONDITIONS

A.	Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  Do not install products under environmental conditions outside manufacturer's absolute limits.

PART 2  PRODUCTS

2.01	COUNTERTOP ASSEMBLIES

A.	Paper Composite Countertops:  Post-consumer recycled and/or FSC-certified paper composite set in petro-free phenolic resin.

1.	Flat Sheet Thickness: [¾”, 1” or 1 ¼”] (To be selected by Architect)

2.	Solid Surfacing Sheet:  Complying with ISSFA-2 and NEMA LD 3; petro-free phenolic resin consisting in part of cashew nut oil, recycled content derived from 100% post-consumer recycled paper, homogenous, non-porous and capable of being worked and repaired using standard woodworking tools; finished with manufacturer’s recommend carnauba wax finish.

a.	Surface Burning Characteristics:  Heat resistant up to 350 degrees Fahrenheit  (175 degrees Celsius). Flame spread Index (20) Class A Rating; Smoke developed Index (110) Class A Rating; when tested in accordance with ASTM E 84.

b.	NSF 51 Approved – Food Prep.

c.	Post-Consumer Recycled Content (by weight): minimum 55%

d.	Water Absorption (by weight): maximum 0.82%

e.	Finish on Exposed Surfaces:  Matte, gloss rating of 5 to 20

f.	Warranty: 15-year Limited

g.	Color and Pattern:  As indicated on drawings.

h.	Manufacturer:

1)	PaperStone by Paneltech

Rep: [Include your North Star rep contact information here]

Supplier: North Star Surfaces | 800.393.9784 | www.nssurfaces.com

3.	Finished Edge Treatment: (To be selected by Architect)

4.	Back and End Splashes:  Same sheet material, square top; minimum [_] inches [___ mm] high.

5.	Skirts:  As indicated on Drawings.

2.02	FABRICATION

A.	Fabricator and Installer Qualifications: Minimum [2] [_] years experience in work of this Section.  North Star Surfaces approved.

B.	Fabricate tops and splashes in the largest sections practicable, with top surface of joints flush.

1.	Join lengths of tops using best method recommended by manufacturer.

2.	Fabricate to overhang fronts and ends of cabinets [_] inch/es ([__] mm) except where top butts against cabinet or wall.

3.	Prepare all cutouts accurately to size; replace tops having improperly dimensioned or unnecessary cutouts or fixture holes.

C.	Provide back/end splash wherever counter edge abuts vertical surface unless otherwise indicated.

1.	Secure to countertop with concealed fasteners and with contact surfaces set in waterproof glue.

2.	Height:  [_] inches ([___] mm), unless otherwise indicated.

D.	Solid Surfacing:  Fabricate tops up to 144 inches (3657 mm) long in one piece; join pieces with adhesive sealant in accordance with manufacturer's recommendations and instructions.

E.	Wall-Mounted Counters:  Provide skirts and aprons as indicated on drawings, finished to match.

PART 3  EXECUTION

3.01	EXAMINATION

A.	Do not begin installation until necessary substrates/supports have been properly prepared.

B.	If substrate/support preparation is the responsibility of another installer, notify Owner’ Representative of unsatisfactory preparation before proceeding.

C.	Verify that wall surfaces have been finished and mechanical and electrical services and outlets are installed in proper locations.

3.02	PREPARATION

A.	Clean surfaces thoroughly prior to installation.

B.	Prepare surfaces using the methods recommended by North Star Surfaces for achieving the best result for the substrate under the project conditions.

3.03	INSTALLATION

A.	Securely attach countertops to cabinets using concealed fasteners.  Make flat surfaces level; shim where required.

B.	Attach plastic laminate countertops using screws with minimum penetration into substrate board of 5/8 inch (16 mm).

C.	Attach solid surface countertops using compatible adhesive.

D.	Seal joint between back/end splashes and vertical surfaces.

1.	Where indicated use rubber cove molding.

2.	Where applied cove molding is not indicated use specified sealant.

3.04	CLEANING

A.	Clean countertops surfaces thoroughly.

3.05	PROTECTION

A.	Protect installed products until completion of project.

B.	Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION